## Slide 1
150 kW DC Fast Charger
Modular, Open-Source, SiC-Based EV Charging Infrastructure
In-House Power Electronics
30 kW SiC modules (Rev 0.7)
Open-Source Software
EVerest (Linux Foundation Energy)
400V & 800V Compatible
150–1000 VDC output range
Scalable Platform
50 kW to 350 kW configurations
Technical Investor Presentation | February 2026

## Slide 2
2
Market Opportunity
Global DC Fast Charging Infrastructure Demand
~17M units
Global EV Sales (2025)
~2.4M
DCFCs Needed by 2030
$30K–$60K
Avg Commercial Price (150kW)
$21,500
Our BOM @100 Units
KEY INSIGHT
Most DCFC manufacturers use proprietary, vertically integrated software stacks. Our open-source EVerest approach eliminates software licensing costs ($2,000–$5,000/unit for competitors) and vendor lock-in while accelerating time-to-market.
Segment | Units/Year (est.) | ASP | TAM
Highway Corridors | 200,000+ | $35K–$50K | $7B–$10B
Urban Charging Hubs | 300,000+ | $30K–$45K | $9B–$13B
Fleet / Depot Charging | 150,000+ | $35K–$60K | $5B–$9B
Destination / Retail | 100,000+ | $25K–$40K | $2.5B–$4B

## Slide 3
3
Product Overview
150 kW CCS2 DC Fast Charger — Key Specifications
Parameter | Specification
AC Input | 3-phase 400–480 Vac, 50/60 Hz
DC Output Voltage | 150–1000 VDC
DC Output Current | Up to 500 A
Maximum Power | 150 kW (5× 30 kW modules)
Peak Efficiency | >96% (SiC-based)
Power Factor | >0.99
Connector | CCS Combo 2 (CCS1 optional)
Charging Time (80%) | 400V: 20–30 min · 800V: 15–20 min
Software | EVerest (Linux Foundation Energy)
Cooling | Sealed cabinet + clip-on HVAC
Enclosure | IP55 target
Standards | IEC 61851, ISO 15118, OCPP 2.0.1
EFFICIENCY
>96%
SiC MOSFETs throughout
VOLTAGE RANGE
150–1000V
400V + 800V EV compatible
SCALABLE
50–350 kW
Same platform, add modules
UPTIME
>98%
N+1 redundancy, hot-swap

## Slide 4
4
System Architecture
4-Level Hierarchical Control with Domain-Isolated CAN Buses
LEVEL 3: CLOUD / BACKEND CSMS (OCPP 2.0.1) · Fleet Management · Billing │ WebSocket / 4G / Ethernet LEVEL 2: STATION CONTROLLER CM5 Main Controller (Linux + EVerest) EvseManager · EnergyMgr · OCPP · Auth · ISO 15118 SafetySupervisorBSP · PowerModuleDriver · HvacDriver │ CAN #2 │ CAN #1 (FD) │ CAN #3 LEVEL 1: MODULE CONTROLLERS Safety Supv. PDU-Micro Master HVAC Unit (STM32, SIL2) (Module 0 PIM) (STM32/RP2350) │ │ │ │ M1 M2 M3 M4 (30kW each) LEVEL 0: HARDWARE Gate Drivers · Sensors · Contactors · Actuators
Design Principles
Safety-critical functions on dedicated STM32 (SIL 2) — never on Linux
Three independent CAN buses isolate safety, power, and thermal domains
Hardware interlock chain operates independently of all software
EVerest microservices communicate via MQTT — modular and testable
CM5 monitors safety but does NOT own the safety loop
PDU-Micro modules self-coordinate via droop-based current sharing

## Slide 5
5
Modular Power Architecture
5× 30 kW Hot-Swappable Modules — Scalable to 350 kW
Configuration | Modules | Power | BOM @100 | BOM @500
Single CCS2 | 5× 30 kW | 150 kW | $21,503 | $19,486
Dual CCS2 (shared) | 5× 30 kW | 150 kW | ~$25,700 | ~$23,700
Single CCS2 | 10× 30 kW | 300 kW | ~$32,900 | ~$28,900
Dual CCS2 | 12× 30 kW | 350 kW | ~$36,900 | ~$32,900
Hot-Swappable
Replace modules without powering down the entire system. Reduces MTTR to minutes.
N+1 Redundancy
Optional extra module ensures continued operation during single-module failure.
Graceful Degradation
Module failure reduces power proportionally — charger stays operational at reduced output.
Field-Scalable
Start at 150 kW, upgrade to 300 kW by adding modules. Same cabinet, same software.

## Slide 6
6
Power Module — PDU-Micro (30 kW)
In-House Designed SiC Power Converter — Core IP
Parameter | Specification
Rated Power | 30 kW continuous
PFC Topology | Vienna Rectifier, 140 kHz
DC-DC Topology | 3-phase Interleaved DAB
SiC Devices (PFC) | MSCSM120VR1M16CTPAG module
SiC Devices (DAB) | MSC080SMA120B discrete
Output Voltage | 150–1000 VDC
Output Current | 100 A per module
DC Bus | 700–920 VDC (adaptive)
Controller | Dual dsPIC33CH512MP506
Communication | CAN-FD 500k/2M bps
Peak Efficiency | 96.3% (system-level)
Status | Rev 0.7, firmware in development
$1,806
Unit Cost @100
$1,436
Unit Cost @500
$60/kW
Cost per kW @100
$48/kW
Cost per kW @500
Top Cost Drivers:
DAB SiC MOSFETs — 23%
Vienna PFC module — 13.3%
PCB fabrication — 13%

## Slide 7
7
Safety Architecture
Dual-Layer: Hardware Interlock Chain + SIL 2 Software Supervision
+24V Safety Supply │ ▼ E-STOP (NC) ─── Door Interlock (NC) ─── IMD Contact (NC) │ │ RCD Contact (NC) ─── Thermal Trip (NC) ─── Safety Relay │ ▼ OUTPUT: AC Contactor · DC Contactor · Pre-charge Relay ANY BREAK IN CHAIN = IMMEDIATE SHUTDOWN CM5/EVerest MONITORS but does NOT own the safety loop
Protection | Response | Method
Over-Voltage (OVP) | < 1 µs | Hardware comparator
Over-Current (OCP) | < 1 ms | Safety supervisor ADC
Ground Fault | < 30 ms | IMD relay (Bender)
Insulation Failure | CableCheck | IMD measurement
CM5 Heartbeat Loss | 2 s timeout | Orderly shutdown
Contactor Weld | Post-open | Aux NC + voltage verify
E-Stop | Immediate | Hardware loop break
States: INIT → IDLE → AC_CLOSE → PRECHARGE → DC_CLOSE → CHARGING → SHUTDOWN → FAULT
Certification Target: IEC 61508 SIL 2 / ISO 13849 PLd
Dedicated STM32 bare-metal controller · MISRA C:2012 · >90% branch coverage · FMEA documentation

## Slide 8
8
Software Stack — EVerest Framework
Open-Source Charging OS — Linux Foundation Energy
┌───────────────────────────────────────────┐ │ APPLICATION LAYER │ │ EvseManager · EnergyManager · Auth · OCPP │ ├───────────────────────────────────────────┤ │ MIDDLEWARE LAYER │ │ ISO 15118 · OCPP 2.0.1 · IEC 61851 │ │ Safety State Machine │ ├───────────────────────────────────────────┤ │ HARDWARE ABSTRACTION LAYER │ │ CAN · Ethernet · GPIO · UART · SPI │ ├───────────────────────────────────────────┤ │ LINUX OS (CM5: 4-core ARM, 4GB) │ └───────────────────────────────────────────┘
Why EVerest
$0 licensing — Apache 2.0 open source
Pre-built ISO 15118, OCPP, IEC 61851 stacks
Microservices via MQTT — independent processes
Linux Foundation Energy backing — major OEM support
Conformance-tested protocol implementations
Active community with regular releases
Custom EVerest Modules (Our IP)
SafetySupervisorBSP
CAN #2 bridge to STM32 evse_board_support, isolation_monitor, ac_rcd, connector_lock
PowerModuleDriver
CAN-FD bridge to PDU-Micro master power_supply_DC, powermeter, module shedding
HvacDriver
CAN #3 bridge to HVAC unit thermal_management, derating logic

## Slide 9
9
Communication & Protocol Stack
Standards-Compliant Vehicle and Network Communication
Vehicle Side (EV ↔ Charger)
Protocol | Standard | Function
Control Pilot | IEC 61851-1 | Basic signaling (States A–F)
PLC (HomePlug GreenPHY) | ISO 15118-3 | Physical layer for HLC
DIN SPEC 70121 | DIN 70121 | Legacy DC fast charging
ISO 15118-2 | ISO 15118-2 | Plug & Charge, smart charging
Network Side (Charger ↔ Backend)
Protocol | Version | Function
OCPP | 2.0.1 | Remote monitoring, billing
TLS | 1.2/1.3 | Secure Plug & Charge certs
MQTT | Internal | EVerest inter-module messaging
HTTP/REST | Service | Diagnostic web UI
Internal Communication Buses
Bus | Speed | Path | Function
CAN #1 (CAN-FD) | 500k/2M bps | CM5 ↔ PDU-Micro modules | Power control & telemetry
CAN #2 | 500 kbps | CM5 ↔ Safety Supervisor (STM32) | Safety state, contactor control
CAN #3 | 250 kbps | CM5 ↔ HVAC Unit | Thermal management
Connectivity: Ethernet (LAN) · 5G Modem (WAN) · WiFi (Service) · PoE Switch · PLC Modem (ISO 15118)

## Slide 10
10
Thermal Management — Clip-On HVAC
Sealed Cabinet with External Heat Rejection
HVAC CLIP-ON UNIT MAIN CABINET ┌─────────────────┐ ┌─────────────────┐ │ Condenser + │ │ Power Modules │ │ Compressor │ │ M1 M2 M3 M4 │ │ │ │ │ M5 │ │ Evaporator │ Cold Air │ │ │ Coil ══════════════> │ Internal │ │ │ │ │ Heatsinks │ │ Blower Fans │ Hot Air │ │ │ <══════════════ │ Hot Air Return │ │ │ │ │ │ HVAC Controller │◄─CAN#3──►│ CM5 Main ECU │ └─────────────────┘ └─────────────────┘ Internal air NEVER mixes with ambient → IP55 sealed
Parameter | Specification
Cooling Capacity | 15–25 kW thermal
Airflow | 2,000–4,000 CFM (variable)
Operating Range | -20°C to +50°C ambient
Refrigerant | R-410A or R-32
Mounting | Side, rear, or top clip-on
Interface | CAN bus + 24V power
Serviceability | Field-replaceable, single unit
THERMAL DERATING CHAIN
Cabinet temp rising → HVAC signals via CAN #3 → EnergyManager reduces output power → Prevents thermal shutdown
Modes: Idle → Pre-Cool → Active Cooling → Max Cooling → Derating

## Slide 11
11
Competitive Analysis
150 kW Class DC Fast Chargers
Feature | Our Design | ABB Terra 184 | Tritium PKM150 | Delta UFC 150 | Kempower S
Max Power | 150 kW (to 350) | 180 kW | 150 kW | 150 kW | 40–600 kW
Efficiency | >96% (SiC) | 95% | ~95% | >94% | N/A
DC Output | 150–1000V | 150–920V | 150–920V | 200–1000V | 50–920V
Max Current | 500 A | 200 A | 350 A | 500 A | 500 A
IP Rating | IP55 (target) | IP54 | IP65 | IP55 | IP54
Software | EVerest (open) | Proprietary | Proprietary | Proprietary | Proprietary
SiC MOSFETs | Yes | Unconfirmed | Unconfirmed | Unconfirmed | Unconfirmed
OCPP | 2.0.1 | 1.6J | 1.6J / 2.0.1 | 1.5S / 1.6J | 1.6J / 2.0.1
Est. Retail | $35K–40K | $40K–50K | $35K–45K | $30K–45K | $35K–50K
Our Differentiators:
» Open-source software — no vendor lock-in, no licensing fees
» SiC throughout — highest efficiency in class
» Full 1000V output — future-proofed for 800V EV wave
» Modular power — same platform scales 50–350 kW
» In-house power electronics — full control of cost and supply chain

## Slide 12
12
Bill of Materials Breakdown
150 kW Single CCS2 — Component Cost @100 Units
Power Modules (5×30 kW)
$10,087 (46.9%)
CCS Connector + Cable
$2,180 (10.1%)
Cabinet and Enclosure
$2,145 (10.0%)
DC Output Protection
$1,785 (8.3%)
HVAC Clip-On Unit
$1,720 (8.0%)
AC Input and Protection
$1,496 (7.0%)
Control Electronics
$730 (3.4%)
Cooling System
$635 (3.0%)
Networking + Comms
$375 (1.7%)
User Interface
$200 (0.9%)
Auxiliary PSU
$150 (0.7%)
TOTAL BOM
$21,503
Volume | BOM Cost | Target Retail | Gross Margin
@100 units | $21,503 | $35,000–40,000 | 40–46%
@500 units | $19,486 | $30,000–35,000 | 35–44%

## Slide 13
13
Cost Optimization Roadmap
Path to Further BOM Reduction
Initiative | Savings/Unit | Timeline
Chinese SiC alternatives (DAB MOSFETs) | $500–$650 | Near-term
Volume pricing on COTS (CCS, contactors) | $1,000–$1,500 | @500+ units
PCB panel optimization + assembly volume | $300–$500 | @500+ units
Backplane redesign (simplified busbar) | $100–$200 | Rev B
In-house HVAC manufacturing | $300–$500 | Year 2
$21,503
BOM @100 (Current)
$19,486
BOM @500
$16,500–$17,500
Projected BOM @1000
~47%
Gross Margin @1000
SOFTWARE COST ADVANTAGE
Competitors spend $2,000–$5,000 per unit on proprietary software licensing. Our EVerest-based stack has $0 per-unit software cost — a structural margin advantage at every volume.

## Slide 14
14
Standards & Certification Plan
International Compliance Matrix
Standard | Scope | Status
IEC 61851-1 | General EV charging requirements | Design phase
IEC 61851-23 | DC charging station requirements | Design phase
IEC 62368-1 | Electrical safety | Testing planned
IEC 61000-6-2/6-4 | EMC (emissions + immunity) | Pre-compliance M11
ISO 15118-2/3 | Vehicle-to-grid communication | EVerest pre-certified
ISO 13849 (PLd) | Safety of machinery | Safety supervisor design
IEC 61508 (SIL 2) | Functional safety | Safety supervisor design
OCPP 2.0.1 | Charge point protocol | EVerest (libocpp) certified
UL 2202 | US market certification | Planned for US launch
Certification Bodies
Europe
TÜV — CE, IEC 61851, EMC
North America
UL — UL 2202, NEC Art. 625
India
BIS — IS 17017 (planned)
China
CQC — GB/T standards (future)
Testing Phases:
Type testing (electrical, EMC, safety)
Protocol conformance (CharIN, OCA)
Field testing (installation verification)
SIL 2 / PLd assessment

## Slide 15
15
Development Plan — 14-Month Timeline
8 Parallel Workstreams to Certification-Ready Prototype
M1
M2
M3
M4
M5
M6
M7
M8
M9
M10
M11
M12
M13
M14
WS-1: PDU-Micro Modules
WS-2: CAN Protocol Bridge
WS-3: Safety Supervisor FW
WS-4: EVerest Integration
WS-5: Cabinet Hardware
WS-6: HVAC Controller FW
WS-7: System Integration
WS-8: Certification
CRITICAL PATH: Module Firmware → CAN Bridge → EVerest Modules → System Integration → Certification

## Slide 16
16
Key Milestones
14-Month Execution Plan — Monthly Gate Criteria
Month | Milestone | Gate Criteria
M2 | Safety supervisor board powered | CAN #2 loopback verified
M3 | First PDU-Micro module producing DC | 30 kW output on bench
M4 | CM5 running EVerest | SafetySupervisorBSP ↔ STM32
M5 | PowerModuleDriver controlling 1 module | CAN-FD setpoint control
M6 | Cabinet assembled, 5 modules installed | Backplane wired, mech fit
M7 | HVAC clip-on operational | Thermal derating chain verified
M8 | First complete charging session | ISO 15118 w/ EV simulator
M9 | Full-power 150 kW sustained test | Thermal steady-state OK
M10 | OCPP backend + HMI complete | Remote monitoring live
M11 | EMC pre-compliance pass | EN 55032 Class B
M12–14 | Certification testing complete | IEC 61851, 62368, EMC

## Slide 17
17
Team & Resource Requirements
8–10 Engineers (3–4 Shared from Existing PDU-Micro Team)
Role | Count | Key Skills
Power Electronics Engineer | 1–2 | PDU-Micro hardware, magnetics, thermal
Embedded FW Engineer (Safety) | 1 | STM32, bare-metal C, MISRA C, IEC 61508
Embedded FW Engineer (Controls) | 1–2 | dsPIC33CH, power converter control loops
Linux/EVerest Software Engineer | 1–2 | C++, Linux, EVerest, SocketCAN, MQTT
Protocol Engineer | 1 | ISO 15118, OCPP 2.0.1, CAN bus, PLC
Electrical/Mechanical Engineer | 1 | Cabinet design, busbar, wiring, IP55
HVAC Engineer | 0.5 | Refrigeration, compressor (part-time)
QA / Certification Engineer | 1 | IEC 61851, IEC 62368, EMC, test planning
Team Leverage
Existing PDU-Micro team provides power electronics and embedded firmware capability (3–4 engineers shared)
EVerest open-source community provides protocol stack support, bug fixes, and conformance testing
Standard industrial HVAC components — no custom refrigeration expertise needed full-time

## Slide 18
18
Risk Mitigation
Top Technical Risks & Mitigations
Risk | Impact | Prob. | Mitigation
PDU-Micro firmware delayed | Critical | Med | EVerest SIL simulation decouples CM5 work
CAN-FD adapter incompatibility | High | Med | Verify M1; PEAK PCAN-USB FD backup
ISO 15118 PLC modem EV compat. | High | Med | Test multiple EVs; DIN 70121 fallback
Safety SIL 2 assessment fails | High | Low | Engage assessor M3; design for SIL 2 upfront
Thermal mgmt insufficient @150kW | Med | Low | Thermal budget validated; full-power test M9
OCPP 2.0.1 interop issues | Med | Med | Multiple CSMS vendors; certified libocpp
Current sharing instability (5 mod) | Med | Low | Droop sharing (proven); early bench test
SiC supply chain disruption | Med | Med | Dual-source; 6-month buffer stock
RISK ASSESSMENT: All critical risks have identified mitigations. Highest-risk item (PDU-Micro schedule) is mitigated by software simulation decoupling. No show-stoppers identified.

## Slide 19
19
Deployment Strategy
Three-Phase Market Rollout
Phase 1: Pilot
Months 14–18
5–10 units at controlled sites
Fleet depots, partner locations
6-month field validation
Collect MTBF, reliability data
OTA firmware updates via OCPP
Phase 2: Regional Launch
Months 18–24
50–100 units
Highway corridors, urban hubs
CPO partner integrations
Dual-connector variant
OCPP backend SaaS offering
Phase 3: Scale Production
Year 2+
500+ units/year
300 kW and 350 kW variants
International certifications
In-house HVAC manufacturing
Multi-connector power-sharing
REVENUE MODEL
Hardware Sales · OCPP Backend SaaS (optional) · Maintenance Contracts · Extended Warranty · Power Module Upgrades

## Slide 20
20
Investment Summary
Why Invest Now
Technical Readiness
30 kW SiC power module at Rev 0.7
Core power electronics IP developed
EVerest proven in production globally
Safety designed to SIL 2 from inception
Full documentation package complete
Cost Advantage
BOM: $21,500 @100 → $17,000 @1000
$0 per-unit software licensing
vs. $2K–$5K for competitors
Target gross margin: 40–47%
In-house design = supply chain control
Market Position
Only open-source SW + in-house HW DCFC
Highest efficiency in class (>96% SiC)
Full 1000V — ready for 800V EV wave
One platform: 50–350 kW
No vendor lock-in for customers
THE ASK
14-month development to certification-ready prototype
8–10 person engineering team (3–4 shared from existing PDU-Micro team)
Pilot deployment of 5–10 units at Month 14
Path to 500+ units/year production by Year 2